## Slide 1
Run the slide show to activate the clickable boxes.
Useful information can be found in the slide notes.
Key concept PEM8.3: Transmitting electricity
P
Prior understanding from earlier stages of learning.
B
Bridge to later stages of learning.
P
Transmission lines
C o n c e p t u a l p r o g r e s s I o n
Talking volts
Transmission lines dissipate less power when they transfer power with a higher transmission voltage and lower current. When current is lower there is a smaller drop in voltage along their length.
Describe the heating effect of current on a conducting wire.
Calculate power dissipated by a wire using P = I2 x R.
Explain the difference between transmission voltage and voltage drop along a wire.
Explain how the equation P = V2/R applies to transmission lines.
Learning focus
As students’ conceptual understanding progresses they can:
Diagnostic questions
Response activities
Power dissipation
Transmission current
The right voltage
Hot line
The right power
Predict changes to current through transmission lines using P = I x V.
B
Notes: The boxes containing the titles of the diagnostic questions and response activities are clickable links that will take you to the starting slide for each activity in this presentation.
In edit mode, hold down the Ctrl key and left-click the box.
In slide show mode, simply left-click the box.
Click the ‘Home’ button at the top right of the final slide of each activity to return here.

## Slide 2
Section 1: Diagnostic questions
A zip file containing all the resources for this key concept can be downloaded from
www.BestEvidenceScienceTeaching.org
The zip file provides:
Teacher guidance for this key concept, including a summary of the research evidence on relevant preconceptions and misunderstandings.
A full set of editable and printable student sheets and teacher notes for each diagnostic question. The teacher notes include a summary of research evidence, guidance for using the activity, expected answers and suggestions of how to respond to students’ misunderstandings.
Use diagnostic questions to identify quickly where your students are in their conceptual progression, and what preconceptions and misunderstandings they may have.
Then decide how to best focus and sequence your teaching.
Use further diagnostic questions and response activities to move students’ understanding forwards.

## Slide 3
A big current flows through power lines.
The bigger the current, the hotter the wires.
When the wires are hotter, they dissipate more power.
Hot line
Notes: From key concept PEM8.3: students should be able to describe the heating effect of current on a conducting wire.
Common misunderstandings: all the electrons in a current flow from the battery (or generator).
Avoid saying: electrons flow from the generator.
Do say: outer electrons move very quickly in all directions – and overall move slowly in the direction of current (in this case an alternating current).
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.
Image from Shutterstock
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 4
A
Electrons are causing metal ions to vibrate faster.
B
Electrons are moving along the wire more quickly.
C
More electrons are moving through the wire.
I am sure this is right
I think this is right
I think this is wrong
I am sure this is wrong
Hot line
Why does a bigger current heat up the power lines?
Home
What do you think about each statement?
Notes: Expected answers: Statements A and B are right; and statement C is wrong.
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.

## Slide 5
A wind turbine has a power of 2 MW (2 000 000 W).
The voltage across it is 1000 V.
Transmission current
Power lines connect the wind turbine to the national grid.
A step-up transformer makes the transmission voltage 275 000 V
Notes: From key concept PEM8.3: students should be able to predict changes to current through transmission lines using P = I x V.
Common misunderstandings: the bigger the transmission voltage, the bigger the transmission current; and the voltage drop across the length of a transmission line is the same as the transmission voltage.
Avoid saying: voltage or potential difference
Do say: transmission voltage
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.
Image by PublicDomainPictures from Pixabay
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 6
What happens to current when transmission voltage is increased?
Transmission current
A
Current decreases.
B
Current stays the same.
C
Current increases.
Home
Notes: Expected answer: A
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 7
The power an electrical device has is calculated using P = I x V.
The resistance of the device is calculated using R = .
Power dissipation
V
I
Rearranging the resistance equation:
Substituting this into the power equation:
Which gives:
V = I x R
P = I x (I x R)
P = I2 x R
V is the voltage across the device.
I is the current through the device.
R is the resistance of the device.
P is the power of the device.
Notes: From key concept PEM8.3: students should be able to calculate power dissipated by a wire using P = I2 x R.
Common misunderstandings: the voltage drop across the length of a transmission line is the same as the transmission voltage.
Avoid saying: electrical energy or electrical power.
Do say: energy and power.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 8
P = I x R
2
A transmission line has a resistance and is heated by current.
It is warmer than its surroundings and dissipates power.
Power dissipation
C
Nine times more power is dissipated.
A
Three times more power is dissipated.
B
Six times more power is dissipated.
1. What happens to the amount of power dissipated if the current through a transmission line is tripled?
Notes: Expected answer: C
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.
Image from Shutterstock.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 9
2. What happens to the amount of power dissipated if the current through a transmission line is halved?
Power dissipation
B
The same amount of power is dissipated.
C
Four times less power is dissipated.
P = I x R
2
A
Four times more power is dissipated.
Home
Notes: Expected answer: C
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 10
The right voltage
The transmission voltage at the start of these power lines is 400 kV.
(400 kV = 400 000 V)
Notes: From key concept PEM8.3: students should be able to explain the difference between transmission voltage and voltage drop along a wire.
Common misunderstandings: the voltage drop across the length of a transmission line is the same as the transmission voltage.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.
Image by Silberfuchs from Pixabay.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 11
What is the transmission voltage at the end of the transmission lines?
The right voltage
D
Exactly 0 kV.
B
A little less than 400 kV.
C
About 200 kV.
A
Exactly 400 kV.
Home
Step-up transformer
Step-down
transformer
400 kV
?
Notes: Expected answer: B
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 12
The power an electrical device has is calculated using P = I x V.
The resistance of the device is calculated using R = .
The right power
Rearranging the resistance equation:
Substituting this into the power equation:
Which gives:
I =
P = x V
P =
V
I
V
R
V
R
V2
R
Notes: From key concept PEM8.3: students should be able to explain how the equation P = V2/R applies to transmission lines.
Common misunderstandings: the voltage drop across the length of a transmission line is the same as the transmission voltage.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.
From key concept PFM6.2: students should be able to calculate forces using 𝑭=𝑚 𝒂 and rearrange this equation.
Common misunderstandings: Students may be able to use Newton’s second law when performing calculations, but a superficial knowledge of the use of formulae may mask qualitative misunderstandings and misconceptions.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 13
A
P = power transferred along a wire.
B
V = voltage drop across the length of a wire.
C
R = resistance of the whole length of a wire.
I am sure this is right
I think this is right
I think this is wrong
I am sure this is wrong
The right power
Home
What do you think about each statement?
How do the variables in P = relate to a transmission line?
V2
R
Step-up transformer
Step-down
transformer
400 kV
Notes: Expected answers: Statements B and C are right; and statement A is wrong.
A breakdown of what each choice tells you about students’ understanding or misunderstanding can be found in the teacher notes for this activity.

## Slide 14
Section 2: Response activities
A zip file containing all the resources for this key concept can be downloaded from
www.BestEvidenceScienceTeaching.org
The zip file provides:
Teacher guidance for this key concept, including a summary of the research evidence on relevant preconceptions and misunderstandings.
A full set of editable and printable student sheets and teacher notes for each response activity. The teacher notes include a summary of research evidence, guidance for using the activity and expected answers.
Response activities encourage students to talk and think about what they’re thinking (metacognition).
This challenges students’ misunderstandings, facilitates meaning-making, and develops and consolidates their scientific understanding.

## Slide 15
Transmission lines
In this model, transformers make the transmission voltage high and the current low.
The model is safe because:
It uses a low voltage a.c. supply of no more than 2 V
The voltage in the transmission lines is no more than about 28 V
The step-down transformer is connected the right way round.
Step-up transformer
Step-down transformer
50
turns
600
turns
600
turns
50
turns
Notes: From key concept PEM8.3: students should be able to predict changes to current through transmission lines using P = I x V; and to calculate power dissipated by a wire using P = I2 x R.
Common misunderstandings: the bigger the transmission voltage, the bigger the transmission current; and the voltage drop across the length of a transmission line is the same as the transmission voltage.
Avoid saying: voltage; and electrical energy or electrical power.
Do say: transmission voltage; and energy or power
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 16
Transmission lines
Predict
How bright the second bulb will be:
with the transformers
without the transformers.
Explain
In each case, why do you think the bulb will be this bright?

## Slide 17
Transmission lines
Observe
How bright is the second bulb:
with the transformers?
without the transformers?
Explain
Were your prediction and explanation correct?
Try to improve your first explanation to explain what happened more clearly.
Watch a demonstration of the transmission lines.
Home
Notes: Expected answer: with the transformers the second bulb is bright, and without the transformers it is very dim (or unlit).
A more detailed answer, with an explanation can be found in the teacher notes for this activity.

## Slide 18
Talking volts
Two different voltage measurements relate to transmission lines:
transmission voltage
voltage drop along the length of a transmission line.
Step-up transformer
Step-down
transformer
400 kV
390 kV
1 kA through each line
(1 kA = 1000 A)
Notes: From key concept PEM8.3: students should be able to explain the difference between transmission voltage and voltage drop along a wire; and explain how the equation P = V2/R applies to transmission lines.
Common misunderstandings: the voltage drop across the length of a transmission line is the same as the transmission voltage.
Student sheets and teacher notes for this activity contain printable and editable worksheets, together with teacher support materials.

## Slide 19
Talking volts
Jasper: The power transmitted is about 400 000 x 1000.
Leon: The resistance of a transmission line can be calculated using R = P/I2.
Mya: Resistance of a transmission line is about 0.1 Ω.
Keeley: The power dissipated is about 1000 A x 10 000 V.
Some students are talking about calculations they can make for the transmission lines using different voltage measurements.

## Slide 20
Mains power
Some students are talking about calculations they can make for the transmission lines using different voltage measurements.
To answer:
Who is right about the calculations?
  Explain your answer
Who is wrong about the calculations?
  What would you say to help them understand?
Home
Jasper: The power transmitted is about 400 000 x 1000.
Leon: The resistance of a transmission line can be calculated using R = P/I2.
Mya: Resistance of a transmission line is about 0.1 Ω.
Keeley: The power dissipated is about 1000 A x 10 000 V.
Notes: Expected answers: All the students are right
A more detailed answer, with a discussion of what the statements reveal about students’ understanding can be found in the teacher notes for this activity.