## Slide 1: Detecting Fire for the Internet of Things (IoT)
Investigating heat sensors

## Slide 2: Early detection and the IoT
Unfortunately it is all too common to hear stories in the news of people, often young children, dying in house fires.
In most cases there is a short but vital period between the start of a fire and the spread of the fire which traps and kills people.

## Slide 3: Early detection and the IoT
Unfortunately, people can be slow to react and under extreme pressure frequently make poor decisions.
Automated systems respond very quickly and in a predictable way. The internet provides an infrastructure that will enable automated systems to link up and to communicate.

## Slide 4: Detecting a fire
Key to such an automated system is the ability to detect the fire.
How to detect a fire:
What would be changed by the fire?
How could the changes be detected?
Is there a change that could be measured/quantified?

## Slide 5: Detecting a fire
carbon
Smell
Fire
Smoke
Heat
Gases
burning
cooking
irritating
soot
ash
CO
CO2
SO2
NO2
flame
sparks
temperature increase
cyanide
light

## Slide 6: Detecting a fire - sensing smoke

## Slide 7: Detecting a fire - sensing smoke

## Slide 8: Bimetal strip temperature sensor

## Slide 9: Bimetal strip temperature sensor
The metal part of the bimetal temperature sensor is made from a strip of brass and a strip of iron.
When the strip is heated, the brass expands more than the iron.
This causes the strip to bend with the brass on the outside of the curve and the steel on the inside.

## Slide 10: Bimetal strip temperature sensor

## Slide 11: Detecting a fire - sensing heat
Your challenge this lesson is to design, make, test and refine a device that can sense a rise in temperature and trigger an electrical response.

## Slide 12: Input process output
There are three aspects to a fire alarm.
Some form of input (produced by the fire) that can be detected by a sensor.
A processor that ‘decides’ if the alarm needs to sound.
Some form of output that alerts the people in the house, usually a loud noise.
Input (rise in temperature)
Process (when temperature reaches a threshold, close a switch)
Output (switch on alarm)

## Slide 13: Bimaterial strip temperature sensor
You are going to make a temperature sensor based on a bimaterial strip made from aluminium and paper.
You will then place your bimaterial strip into the gap in your circuit and use it to close a switch when the temperature reaches a threshold level.
The alarm will sound.

## Slide 14: Electrical circuit
Using a battery, buzzer (alarm) and wires, you will build a series circuit with a gap somewhere in the circuit.

## Slide 15: Electrical circuit
The gap in the circuit is where you will place the temperature sensor.

## Slide 16: Bimaterial strip temperature sensor
Apparatus
Two wooden blocks
Buzzer
Batteries
Wires to connect up the circuit
Aluminium foil to make four strips 8 cm by 1 cm
Self-adhesive paper labels to make four strips 6 cm by 1 cm
Scissors
Sticky tape
Tealight candle
Tongs
Heatproof mat

## Slide 17: Bimaterial strip alarm circuit

## Slide 18: Bimaterial strip alarm sensor
COLD - switch open HOT - switch closed

## Slide 19: Bimaterial strip alarm operation

## Slide 20: Discussion questions
What did you do to make it less sensitive?
What did you do to make it more sensitive?
Evaluate the bimaterial strip as a fire sensor. What are its advantages and what are its disadvantages?
How might such a device be incorporated into the IoT to produce a more rapid response to a fire?

## Slide 21: Cisco Little Big Futures
Image credits:
Thermistor: By Ansgar Hellwig (photo taken with Canon PowerShot G3) [CC BY-SA 2.0 de (http://creativecommons.org/licenses/by-sa/2.0/de/deed.en)], via Wikimedia Commons
IOT drawing: By Wilgengebroed on Flickr [CC BY 2.0 (http://creativecommons.org/licenses/by/2.0)], via Wikimedia Commons
Bluetooth and Wi-Fi logos are registered trademarks in the public domain.