## Slide 1
Spirit of
Innovation
STEAM
RESOURCES
Spirit of Innovation
Year Four
PowerPoint – Pneumatics & Hydraulics

## Slide 2: Hydraulics

## Slide 3: Hydraulics
A hydraulic system is one that uses the pressure of a liquid to perform mechanical work.
A
B
If pressure is put on piston A, the same pressure will be transmitted to piston B
When a liquid is enclosed in a space and a pressure is applied, the pressure is transmitted equally to all parts of the liquid, as liquid cannot be compressed.
You will see the liquid will move from A to B, making piston B rise.
In many cases the liquid used is oil as it lubricates the machine as well.

## Slide 4: Hydraulics
A
B
Again, if pressure is put on piston A the same pressure will be transmitted to piston B
This hydraulic system is a force multiplier. Note, the smaller piston A has to move a larger distance the piston B.
However, this time the syringe B is larger. The same amount of fluid transmits from A to B. But Piston B rises slower and moves less distance.
If one piston is made larger than the other piston, it can raise a larger load.

## Slide 5: Use of Hydraulics

## Slide 6: Pneumatics
Pneumatics is a similar to hydraulics, but rather than the movement of water or oil, it uses gas or air.
This can be demonstrated easily using the items below.
Materials: Cardboard box Sticky Tape Scissors Syringe/lungs PVC tubing

## Slide 7
Pneumatics
Make a hole in the side of the box in which to thread the tubing. Attach a balloon to the end of the tubing inside the box. Use sticky tape to make an airtight seal. Attach a syringe to the other end of the tubing. Press the syringe. Or you can you your own breath and blow!

## Slide 8
Pneumatics
The air from the syringe or your lungs blows up the balloon which in turns forces the lid of the box open.

## Slide 9: Pneumatics
A pneumatic system is one that uses the pressure of a gas to perform mechanical work.
A
B
If pressure is put on piston A, the same pressure will be transmitted to piston B
When a gas is enclosed in a space and a pressure is applied, the pressure is transmitted equally to all parts of the gas, as gas cannot be compressed.
You will see the gas will move from A to B, making piston B rise.
In this case the gas used is air.

## Slide 10: Use of Pneumatics

## Slide 11
Materials: Cardboard Sticky Tape Scissors Pens Ruler Pencil Glue gun Syringe (2) PVC tubing | Various: Recycled materials String Paper clips Split pins Blank blueprint

## Slide 12
Can you design your own plane with hydraulic undercarriage?

## Slide 13
Undercarriage pneumatic design
Project name | Spirit of Innovation | 
Max Power | 750 kW | 
Top Speed | 300+ MPH | 
Range | 200 miles | 
Development | 24 months | 
Collaborators |  | 
Name of Designer: |  | 
Introducing the world’s fastest electric aeroplane
Year 4
Pneumatics

## Slide 14
Undercarriage pneumatic design
Project name | Spirit of Innovation | 
Max Power | 750 kW | 
Top Speed | 300+ MPH | 
Range | 200 miles | 
Development | 24 months | 
Collaborators |  | 
Name of Designer: |  | 
Introducing the world’s fastest electric aeroplane
Year 4
Pneumatics

## Slide 15
Materials: Cardboard Sticky Tape Scissors Box with lid Pens Ruler Pencil | Glue gun Syringe (8) PVC tubing Small ball Food colouring/coloured tape Water/air Stop watch

## Slide 17
These resources have been brought to you by