## Slide 1: How high will it go!
Finding the height achieved by a flying object using trigonometry

## Slide 2
Stay safe
Whether you are a scientist researching a new medicine or an engineer solving climate change, safety always comes first. An adult must always be around and supervising when doing this activity. You are responsible for:
ensuring that any equipment used for this activity is in good working condition
behaving sensibly and following any safety instructions so as not to hurt or injure yourself or others
Please note that in the absence of any negligence or other breach of duty by us, this activity is carried out at your own risk. It is important to take extra care at the stages marked with this symbol: ⚠

## Slide 3: Using trigonometry to find height
Trigonometry is a branch of mathematics that deals with the relationship between the sides and angles of a triangle
Pythagoras’ theorem allows calculations based on triangles if two sides are known.
Engineers don’t always know the length of two sides
Other methods are needed for calculations related to triangles

## Slide 4: Identifying the sides of a triangle
Hypotenuse
Opposite
Adjacent
θ
The opposite is always opposite the angle being used for calculations
The adjacent is always next to the angle being used for calculations
The hypotenuse is always the longest side in a right angled triangle.

## Slide 5: Tangent
Opposite
θ
Tangent θ = Opposite ÷ Adjacent
Adjacent
Notes: .

## Slide 6: Tangent
41
30
θ
Tangent θ = Opposite ÷ Adjacent
= 41 ÷ 30 = 1.367
If you know the tangent θ you can find the angle:
On the calculator tan-1 1.367 = 53.8o
If you know the angle you can find the tangent:
On the calculator tan 53.8 = 1.367
Notes: .

## Slide 7: Tangent
Opposite
Adjacent
θ
Tangent θ = Opposite
Adjacent
Tan
Adj
Opp

## Slide 8: Tangent example
X
1.15 m
From the diagram you need to calculate the length X
Using the formula triangle, hold your finger over the “ Opp” to indicate the calculation (tan θ x Adj)
The tan of 50o is 1.192 (from calculator)
X = Opposite = 1.15 x 1.192 = 1.37 m
50o
Tan
Adj
Opp

## Slide 9: Clinometer ⚠
Print out the worksheet onto thin card
Carefully cut out the protractor and the slide
Punch two holes using a sharp pencil with an eraser behind the card ⚠
Attach the protractor and slider with a brass paper fastener

## Slide 10: Measure the height experiment
Work with a partner
One of you inflates and holds the balloon at head height
The second holds the clinometer level with the balloon
Stand a set distance apart e.g. 5 m

## Slide 11: Ready for balloon release
Level
5 m
Notes: Discuss the brief and design criteria with learners.

## Slide 12: What’s the angle?
23 degrees
Release the balloon
Raise the slider on the clinometer to match the balloons height
Record the angle

## Slide 13: Record the angle
Print off the recording sheet
Record the angle
Calculate the height

## Slide 14: Tangent example
?
5 m
The unknown length is the opposite
Using the formula triangle, hold your finger over the “ Opp” to indicate the calculation (tan θ x Adj)
The tan of 23o is 0.424 (from calculator)
Opposite = 5 x 0.424 = 2.12 m
23o
Tan
Adj
Opp

## Slide 15: Additional questions
Calculate the unknown side:
?
158 mm
22o
?
128 mm
35o
Tan
Adj
Opp
1.
2.
Notes: Answers: Q1 63.8 mm; Q2 182.8 mm